## Slide 1: Motion Kit (Kit 2)
Motion Foundation Lessons (MFL)
(Lesson Ref: MFL05)
MFL05: Accelerometer MPU6050

## Slide 2: Motion Kit : Contents
Motion Creative Board
Motion Kit Components

## Slide 3: MFL05 : Accelerometer MPU6050
Things Needed

## Slide 4
MFL05 : Accelerometer MPU6050
Arduino Pin | Breadboard
GND (Brown Wire) | Blueline
5V (Red Wire) | Redline
Connections:

## Slide 5
MFL05 : Accelerometer MPU6050
MPU6050 | Arduino Pin
VCC | 5V
GND | GND
SCL | A5
SDA | A4
Connections:

## Slide 6: MFL05 : Accelerometer MPU6050
Include libraries
setup()
Start serial communication
Start I2C communication
Initialize MPU6050 sensor
Check sensor connection
loop()
Read acceleration values (AX, AY, AZ)
Print values on Serial Monitor
Repeat continuously
https://github.com/info-zas/zas-robotics-motion/tree/main/01_FoundationProjects/MFL05_Accelerometer/MFL05_Accelerometer_MPU6050
Code for Lesson MFL05 (MFL05_Accelerometer_MPU6050.ino):

## Slide 7: MFL05 : Accelerometer MPU6050
Execute the same code in the motion creative board
https://github.com/info-zas/zas-robotics-motion/tree/main/01_FoundationProjects/MFL05_Accelerometer/MFL05_Accelerometer_MPU6050
Code for Lesson MFL05 (MFL05_Accelerometer_MPU6050.ino):

## Slide 8: MFL05: Accelerometer MPU6050
Code for Lesson MFL05 (MFL05_Accelerometer_MPU6050_OLED.ino):
https://github.com/info-zas/zas-robotics-motion/tree/main/01_FoundationProjects/MFL05_Accelerometer/MFL05_Accelerometer_MPU6050_OLED
Include libraries
setup()
Start serial communication
Start I2C communication
Initialize MPU6050 sensor
Initialise OLED
Check sensor connection
loop()
Read acceleration values (AX, AY, AZ)
Print values on Serial Monitor and OLED
Repeat continuously