## Slide 1: Motion Kit (Kit 2)
Motion Foundation Lessons (MFL)
(Lesson Ref: MFL02)
MFL02: DC Motor Direction Control Using TB6612

## Slide 2: Motion Kit : Contents
Motion Creative Board
Motion Kit Components

## Slide 3: MFL02 : Direction Control DC Motor with TB6612 Motor Driver
Things Needed

## Slide 4
MFL02 : Direction Control DC Motor with TB6612 Motor Driver
Connections:
Power and Ground connections

## Slide 5
TB6612 Pins | Arduino UNO Pins
PWMA | 5
AIN2 | 4
AIN1 | 6
TB6612 Pins | DC Motor
AO1 | DC Motor
AO2 | DC Motor
MFL02 : Direction Control DC Motor with TB6612 Motor Driver
Connections:
DC Motor connections as below

## Slide 6
https://github.com/info-zas/zas-robotics-motion/blob/main/01_FoundationProjects/MFL02/MFL02/MFL02.ino
setup()
• Set motor driver pins as OUTPUT
(PWM pin, Direction pin 1, Direction pin 2)
loop()
• Set motor speed (0–255)
• Run motor forward for 1 second
• Run motor backward for 1 second
forward()
• Set direction pins for forward motion
backward()
• Set direction pins for reverse motion
MFL02 : Direction Control DC Motor with TB6612 Motor Driver
Code for Lesson MFL02 (MFL02.ino):

## Slide 7
Execute the same code MFL02.ino in the motion creative board
setup()
• Set motor driver pins as OUTPUT
(PWM pin, Direction pin 1, Direction pin 2)
loop()
• Set motor speed (0–255)
• Run motor forward for 1 second
• Run motor backward for 1 second
forward()
• Set direction pins for forward motion
backward()
• Set direction pins for reverse motion
https://github.com/info-zas/zas-robotics-motion/blob/main/01_FoundationProjects/MFL02/MFL02/MFL02.ino
MFL02 : Direction Control DC Motor with TB6612 Motor Driver
Code for Lesson MFL02 (MFL02.ino):

## Slide 8: Applications of DC Motors
Applications of DC Motors
Electric vehicles and battery-powered vehicles
Fans, blowers, and cooling systems
Conveyor belts and material handling systems
Toys and small household appliances
Pumps and compressors
Robotics and simple motion control systems
DC motors are widely used for applications requiring continuous rotation and speed control.