## Slide 1: Motion Kit (Kit 2)
Motion Foundation Lessons (MFL)
(Lesson Ref: MFL12)
MFL12: NeoPixel Strip Control with Rotary Encoder

## Slide 2: Motion Kit : Contents
Motion Creative Board
Motion Kit Components

## Slide 3: MFL12 : NeoPixel Strip
Things Needed

## Slide 4
MFL12 : NeoPixel Strip
NeoPixel Strip | Arduino Pin
VCC | 5V
GND | GND
DI | 12

## Slide 5: MFL12 : NeoPixel Strip
Include required library
Adafruit NeoPixel library
Define parameters
Set NeoPixel data pin
Set number of LEDs
setup()
Initialize NeoPixel strip
Set LED brightness
loop()
Turn ON all LEDs in the strip
Set all LEDs to cyan color
Update LEDs continuously
Code for MFL12 (MFL12.ino)
https://github.com/info-zas/zas-robotics-motion/blob/main/01_FoundationProjects/MFL12/MFL12/MFL12.ino

## Slide 6: MFL12 : NeoPixel Strip
Execute the same code (MFL12.ino) in the motion creative board
https://github.com/info-zas/zas-robotics-motion/blob/main/01_FoundationProjects/MFL12/MFL12/MFL12.ino
Code for Lab M2
Place the NeoPixel strip in J15.

## Slide 7: MFL12_a : NeoPixel Strip Control with Rotary Encoder
Include required library
Adafruit NeoPixel library
Define pin connections
NeoPixel data pin
Rotary encoder CLK and DT pins
setup()
Initialize NeoPixel strip
Set brightness
Read initial encoder state
loop()
Detect rotary encoder rotation
Change color index based on direction
Update NeoPixel strip color
Repeat continuously
Code for MFL13 (MFL12_a.ino):
https://github.com/info-zas/zas-robotics-motion/blob/main/01_FoundationProjects/MFL12/MFL12_a/MFL12_a.ino
Place the NeoPixel strip in J15.

## Slide 8: MFL12_a : NeoPixel Strip Control with Rotary Encoder
Execute the code (MFL12_a.ino) in the motion creative board
Place the NeoPixel strip in J15.
Code for MFL13 (MFL12_a.ino):
https://github.com/info-zas/zas-robotics-motion/blob/main/01_FoundationProjects/MFL12/MFL12_a/MFL12_a.ino